## Slide 1: Power industry: From Regulation to Market… & back to Regulation
Robert Schuman Centre for Advanced Studies
Yannick Perez* & Jean-Michel Glachant**
*CentraleSupélec, & Université Paris-Sud
yannick.perez@u-psud.fr
**Florence School of Regulation
Jean-michel.glachant@eui.eu
Energy Regulation Training – Indian Ocean, 6-8 February 2017

## Slide 2: Outline
Electricity Industry: structures & restructuring
Regulation

## Slide 3: Outline
Electricity Industry structures & restructuring
Regulation

## Slide 4: Part 1: Electricity industry restructuring
Power sector organization models
From traditional regulation to liberalization?

## Slide 5: Various power sector organization models
Model 1
Monopoly
Model 2
Single buyer
Model 3
Wholesale
competition
Model 4
Retail
competition
Sector can become like any other commodity industry
But:
More complexity, regulation, IT infrastructure, etc
More structural changes required to go to

## Slide 6: 4 Power sector organization models
Four representative models (*)
  abstractions, do not describe particular systems
  intermediate cases & variations are possible
Correspond to various structures with varying degrees of monopoly, competition & choice
Public or private ownership is ignored
  Model 1: monopoly at all levels
  Model 2: purchasing agency
  Model 3: wholesale competition
  Model 4: wholesale & retail competition
(*) From “Competition & choice in electricity”, S. Hunt & G. Shuttleworth, John Wiley, 1996

## Slide 7: Model 1: Monopoly (1 or many countries)
Generation
Transmission
Distribution/ Retail
Consumers
Generation
Transmission
Distribution/ Retail
Consumers

## Slide 8: Model 1: Monopoly Description
Full vertical integration
  Some distribution companies may be unbundled
Central planning of generation & network
Cost-of-service remuneration of each vertically integrated utility  regulated tariffs
Wholesale transactions
  between vertically integrated utilities
  between a distributor & a vertically integrated utility
with wheeling transmission charges
Limited incentive regulation is possible
Social policy obligations

## Slide 9: Model 1: Monopoly features
Most risks are passed to consumers
  mistakes in investment, demand forecast, technological obsolescence, etc.
Abuse of social policy obligations (utility as tax collector)
  indigenous fuels, fuel diversity, nuclear moratoria, electricity discounts, local taxes, etc.
Or “popular” opposite: low price, low quality, shortage = low equilibrium
Regulatory lag & “prudent expenditures”
  adequate rate of return to investors
Pressure from cheap potential new entrants

## Slide 10: Model 2: Purchasing agency (single buyer)
IPP
Single buyer
Distribution/ Retailer
Consumer
IPP
IPP
Distribution/ Retailer
Consumer
IPP
Single buyer
Distribution/ Retailer
Consumer
IPP
Distribution/ Retailer
Consumer
Own
generation

## Slide 11: Model 2: Purchasing agency Description (1)
Less vertical integration than model 1
Independent Power Producers (IPPs) compete (or collude) to sell to the single purchasing agency
  competition (e.g. bids) in construction, operation & negotiation of contracts (PPAs) with the single buyer
  mandatory purchase at “avoided cost” (questionable)
Purchasing agency (= Public Policy) is responsible for generation adequacy
Limited economic incentives in “LT credible” PPA contracts
  availability payments, indexation of variable costs

## Slide 12: Model 2: Purchasing agency Description (2)
Cost-of-service, PPA contracts & social policy obligations  regulated tariff
Wholesale transactions: as in model 1. IPPs do not have retail access
Purchasing agency (via consumers’ tariffs) puts the generators’ risk in the PPA contracts
Independence of the purchasing agency becomes a critical issue (economic dispatch & political friendliness: US/ Chinese case)

## Slide 13: Model 2: Purchasing agency Comments
Some competition on the generation side, while the purchasing agency keeps centralized strategic control
Typical drawbacks of centralized planning
Risk of IPPs is passed to consumers  lower capital costs & easier to raise capital
Exquisite control of PPA contracts is needed (corruption)

## Slide 14: Model 3: Wholesale competition
Generator
Wholesale market
Distribution/ Retail
Consumer
Generator
Generator
Distribution/ Retail
Consumer

## Slide 15: Model 3: Wholesale competition Description (1)
Free transactions between distributors & generators, thus sharing risks
Distributors (now multiple purchasing agencies) maintain a monopoly over final consumers  regulated tariffs
Social policy obligations must be charged via regulated tariffs
No central planning of generation, free entry
Generation stranded costs & benefits appear

## Slide 16: Model 3: Wholesale competition Description (2)
Trading arrangements
  open access & ancillary services  system operator
  organized markets (spot, derivatives)  market operator (not a single buyer, but an “auctioneer”)
  bilateral wholesale contracts Generator/Supplier
  IPPs may choose between bilateral contracts & the spot market
  regulated network access charges

## Slide 17: Model 3: Wholesale competition Comments
IPPs may / may not be vertically integrated with distributors (risk of self dealing)
Issues of “market power” are now relevant
Long term “security of supply” is in principle left to the market
Strong incentive to efficiency in generation if real competition in wholesale market
Pressure may come from consumers to go to retail competition

## Slide 18: 4: Both Retail & Wholesale competition
Generator
Power Exchange
Supplier
Qualified
consumer
Generator
Generator
Distributor/ Retailer
Captive
consumer
Supplier
Distributor/ Retailer
Qualified
consumer
Captive
consumer
Wholesale
market
Retail
market

## Slide 19: Model 4: Both Wholesale & Retail competition. basics
All customers have access to competing generators either directly or through their choice of retailer  regulated tariffs only as a back-up option
Social policy obligations only via access tariffs
Complete separation of generation & retailing from the networks (transmission & distribution)

## Slide 20: Model 4: Both Retail & Wholesale competition. More features
The “spot” market Day Ahead becomes essential
Metering consumers becomes a major problem
Generation “stranded costs” & benefits appear 
  “gradual eligibility” of consumers may help
  “vesting contracts” may help
  “levies” via access charges may help
Issues of market power are again relevant
Long term security of supply is in principle left to the market
Strong incentive to efficiency in generation if real competition

## Slide 21: Part 2: Regulation & Liberalization
Power sector organization models
Traditional regulation vs “Liberalization”

## Slide 22: 30 years old drivers for energy liberalisation (= Western World before Donald Trump)
Rethinking & re-inventing government (‘80’s)
      [Reagan, Thatcher, Delors….]
Why not for public services & utilties?
    Telecom, airports, railroads
    Gas & electricity

## Slide 23: Traditional regulation Basic features
Monopolistic geographic franchises
Pervasive public ownership of power utilities
Legal planning & supply obligations
Vertical integration of activities
Centralized economic dispatch
Regulated retail prices based on cost-of-service
Voluntary coordination transactions of limited importance among utilities

## Slide 24: The New Liberal frame Why? (1)
Competition is possible in generation
(wholesale market is feasible)
  Enhanced transmission network capacity  larger relevant markets  no economies of scale in generation
  New generation technologies (CCGT)  smaller size, shorter installation time, reduced environmental impact  long-term marginal costs smaller than average generation costs  good perspectives with new capacity (in theory)

## Slide 25: Changes in fossil fuel generation technology (1)
60’s - 80’s
  typical capacity of coal-fired & nuclear units: 600 to 1000 MW
  long construction time: 6 to 10 years
  decisions on generation expansion were taken long before the capacity was needed
  very large investments and frequent cost overruns
   only large, vertically integrated utilities under cost-of-service remuneration were able to make the necessary investments

## Slide 26: Changes in fossil fuel generation technology (2)
90’s - 00’s (Dash for gas with “CCGT” technology)
  optimal plant capacity may be less than 300 MW
  construction time may be less than 2 years
  much smaller investment per installed kW than other base-load technologies
  wide availability of natural gas
  lower environmental impact / regulatory uncertainty
   investment decisions can be made by smaller & more numerous agents

## Slide 27: The new liberal frame Why? (2)
Competition is possible in supply & in retail market (smart meters & smart phones >> smart Apps & platforms)
  Technological advances in metering, communications & information processing  facilitate multiplicity & variety of commercial transactions (alternative aggregation via Apps)
Favorable economic climate
  Global trend opens financing towards innovation & liberalization; cost of HighTech makes it cheap

## Slide 28: The new liberal frame Why? (3)
Shortcomings of the traditional model
  Illimited governmental intervention
  Conflictive role of Government as owner & as regulator & as consumers advocate
  “Administrative” management (in general)
  Lack of investment because state lacks financing capacity (in some countries)

## Slide 29: The new liberal frame Why? (4)
Additional issues
  Reduce final prices (richer countries) & better align prices with costs (less rich ones)
  Stimulate retail and demand-side activities
  Market-driven retirement of old, dirty & costly generating plants
  Competition for competition’s sake (keep it open: implicit competition)

## Slide 30: The new “liberal” regulation Basic features
Unbundling of activities
  generation & retailing are open to competition
  transmission & distribution remain regulated
  diverse alternatives with system & market operation
End consumer can choose supplier
Wholesale market: organized &/or bilateral
Diverse contracts (physical, financial) to hedge the risk
Operation & investment planning is no longer a centralized activity
Independent regulator

## Slide 31: The new “liberal” regulation Basics
Liberalization
  of the wholesale market
  of the retail market
Restructuring
  unbundling of vertically integrated activities
  action (if needed) on horizontal concentration
Privatization
The need for transition measures
Notes: In addition:
(part of liberalization) Free entry into generation, trading & retailing to promote competition
Reform regulation of residual monopoly segments
Develop efficient transmission network governance & regulatory arrangements to support competitive energy markets

## Slide 32: Outline
Electricity Industry restructuring
Regulation

## Slide 33: Part 2: Regulation
Regulation of markets in general
Competition and competition policy
Regulation in energy network services
Who regulates: the regulatory institution

## Slide 34: Part 2: Regulation
Regulation of markets in general
Competition and competition policy
Regulation in energy network services
Who regulates: the regulatory institution

## Slide 35: Why should economic activities be regulated?
A frame of rules is necessary to the working of markets
  Contract law
  Technical standards, interoperability
  Urban design, planning
  Health, worker safety, consumer protection
  Protection of savers: financial regulation
  International trade
Various levels: local, national, European, world
Regulation has to be constantly adapted

## Slide 36: 1. Regulation in general
Regulation has to be constantly adapted to changing conditions
Regulation
  is not a goal in itself
  is not an ideology
  is an instrument and should be kept as light as possible
De-regulation is a priority whenever conditions allow it

## Slide 37: Part 2: Regulation
Regulation of markets in general
Competition and competition policy
Regulation in energy network services
Who regulates: the regulatory institution

## Slide 38: 2. Competition
liberal rule in a rich economy is competition, for
  efficiency
    prices are higher under monopoly than in competition (static analysis)
    competitive pressure induces cost cutting and search for efficiency (dynamic analysis: efficient companies have higher margins)
    competition induces innovation (dynamic analysis: new products & processes allow higher margins for some time)
  Liberalism: freedom of enterprise, freedom of choice

## Slide 39: 2. Competition policy
competition doesn’t happen spontaneously; needs policy
competition policy removes the obstacles:
  Abuses of dominant position
  Cartels (hence the name: antitrust)
  Growth through mergers & acquisitions
antitrust was developed in the US since 1890, has been one strong point of European development since 1958
removal of barriers and creation of a single market in the European area is a strong competition policy in itself

## Slide 40: Part 2: Regulation
Regulation of markets in general
Competition and competition policy
Regulation in energy network services
Who regulates: the regulatory institution

## Slide 41: 3. Why should energy services be regulated?
Energy networks are a clear case of natural monopoly
Activities different from network services may be organised in competition, but this does not happen easily, so a special competition policy has to be organised
Energy is a primary need and should be guaranteed to all citizens (public service)
Energy is essential to the economic system (strategic resource)

## Slide 42: 3.a. regulation in energy services: networks
  characters of a “natural monopoly”:
    decreasing average cost
    implying that having one producer is socially more efficient than have many
    for the relevant amount of demand
  networks are “essential facilities”, i.e. infrastructures which
    are necessary to competitors for providing services to their customers,
    cannot be replicated economically (or not at all)

## Slide 43: 3. b. activities in competition
Activities being not “network services”:
  Gas exploration, production
  Electricity generation
  Commercial activities
… can be organised in competition
but this does not happen easily, so a special competition policy has to be organised
Special difficulty: the transition from a formerly monopolistic setting

## Slide 44: 3. b. from monopoly to competition
open access to networks is necessary to energy commercial companies (Third Party Access, TPA)
network companies must grant access to all commercial companies at fair conditions and prices
this requires some sort of regulation
  explicit, public regulation, or
  self-regulation with negotiated conditions
European preference for public regulation

## Slide 45: 3. b. the vertically integrated company
the vertically integrated company is the historical model in energy network services
there is a conflict of interest in managing a network and an energy business at the same time:
  Possible cross subsidy in tariff setting
  Possible discrimination in access
  Possible distortions in development of network
European preference for separation of activities (unbundling)

## Slide 46: 3. b. types of unbundling
Unbundling forms:
  Accounting – Managerial – Legal - Ownership
In favour of ownership unbundling:
  the only way to have effective unbundling
  allows lighter regulation
  where public ownership is popular, provides a way out
Against:
  economies of scale (e.g. in buying gas, building infrastructures)
  shareholders rights against forced breakup of enterprise
  defence against foreign, non-European acquisitions
  protection of know-how

## Slide 47: 3. b. retail competition
competition at the wholesale level is undisputed
EU choice of extending free choice and competition to the retail level
It was possible to choose a different model: a Single Buyer to buy wholesale and supply small consumers
retail competition does not work immediately, the switching rate grows slowly
regulators maintain reference tariffs during the transition and invest in information, consumer education

## Slide 48: 3. c. public service
Energy is a primary need and should be guaranteed to all citizens (public service)
Public service obligations are usually imposed upon:
  Network companies:
    connection
    quality of service (interruptions, voltage, gas pressure)
    metering (accuracy, frequency of reading)
    information, complaints
  Energy companies:
    Billing (frequency)
    treatment of people in need
    information, complaints

## Slide 49: 3. d. strategic resource
Energy is essential to the economic system
A balanced mix of primary energy sources (and of fuels) for security of supply
Traditionally a competence of national governments; presently a mix of European institutions, national governments, regulators
Public service and national strategies have been used as arguments for public ownership of energy companies or for protection of “national champions”

## Slide 50: Part 2: Regulation
Regulation of markets in general
Competition and competition policy
Regulation in energy network services
Who regulates: the regulatory institution

## Slide 51: 4. Who regulates? The regulatory institution
A specialised, technical body with tasks:
Consultative
Proposal
Normative, executive:
  set access rules
  set network and other tariffs
  licensing & authorization of facilities
  quality supervision & control
  supervision of competitive behavior (with antitrust authority)
Operative
  request of information, inspection
  sanction
Arbitration and conflict resolution

## Slide 52: 4. Is a regulator necessary?
a competition policy and some self regulation may be enough in very rare and very favorable case
the Competition Authority could:
  prevent and repress abuse of dominant position by the network (system) operators
  ensure competition in the commercial activities
technical regulation could be left to the companies themselves

## Slide 53: 4. Is a regulator necessary?
in fact this is very rarely a good solution since:
  technical regulation can be biased
  the Competition Authority intervenes only ex-post and has trouble in gathering evidence of violations
  high technical contents requires a specialised institution
The choice in favour of having a regulator prevails

## Slide 54: 4. Is regulation temporary?
Will the need for regulation decrease after the first phase of liberalisation: will regulators be unemployed after a transition period?   
Anyway some regulation is required both for the networks (natural monopolies) and for the competitive markets (like in the case of financial markets)   

## Slide 55: 4. Is a regulator necessary?
the future function of regulators depends on:
    the degree of effective competition (structural evolution)
    the growth of self regulation in network companies, market operators
    effective antitrust action
    technical change
    AND THE SOCIAL GOALS: Universal Access to Energy ; COP21 & 2050 compatible Decarbonization

## Slide 56: 4. An independent institution
In a liberal setting the regulator should be independent with respect to the regulated companies
And also with respect to Goverment? Not quite
Yet there are reasons in favour of independence
  a clear and stable framework is a condition for private investment
  Government is subject to pressure and inclined to compromise
  Government protects national companies, specially when is owner
  general “advantage of tying one’s hands” (as in the case of the central bank)

## Slide 57: 4. Legitimacy
Issue of democratic legitimacy: a risk of technocracy?
  Legitimacy does not depend only on popular election!
Legitimacy of an independent institution is based on:
    Legal basis, precisely defiined mandate
    Appointment procedure, to assure competence, ethical standard
    Incompatibilities, to avoid conflict of interest
    Transparent decisions, predictable procedures
    Consultation of interested parties
    Accountability to Parliament (better than to Government)
    Financial provisions
    Judicial review

## Slide 58: End!