## Slide 1
Jean-Michel Glachant, Director FSR
IIT Kanpur – Center for Energy Regulation
10 October 2018
EU Electricity Regulation - Present & Future

## Slide 2: Table of content
EU Electricity Wholesale Market Design (Regulation)
  [1] El. Day-Ahead Energy Markets & European Coupling
  [2] Network codes as EU Market Design
EU Electricity System Long Term (Analysis)
  [3] Mid term generation adequacy forecast 2017
  [4] Ten Year Network Development Plan 2018
EU Electricity Transition – very long term (Vision)
  [5] How to surf on innovation waves… >> Tomorrow

## Slide 3: What a mess? Or what a chess?
Day-ahead market
Intraday markets
Balancing market
Reserves/ ancillary services markets
Explicit auctions for transmission capacity
Implicit auctions
Market coupling
Market splitting
Capacity markets
Bilateral / OTC
Long term contracts
Flexibility market
Base load product
Peak load product
Congestion management

## Slide 4: [1] El. Day-Ahead Energy Markets & European Coupling

## Slide 5: The case of Europe
Are the European markets coupled or national?
Intraday
market
(energy B)
Balancing
Mechanism
(Power B)
Intraday
Markets
(energy A)
Balancing
Mechanism
(Power A)
Country B
Country A
Day ahead
Market
(energy B)
Day ahead
Market
(energy A)
Day ahead
Market
(transmission A-B)
Intraday
market
(transmission A-B)
Interconnection
capacity
Balancing
mechanism
(transmission A-B)
‘’Gate
Closure’’

## Slide 6: What El. Wholesale markets to integrate? How EU does it ?
Intraday
market
(energy B)
Balancing
Mechanism
(energy B)
Intraday
Markets
(energy A)
Balancing
Mechanism
(energy A)
Country B
Country A
Day ahead
Market
(energy B)
Day ahead
Market
(energy A)
Day ahead
Market
(transmission A-B)
Intraday
market
(transmission A-B)
Interconnection
capacity
Time
Space
Balancing
mechanism
(transmission A-B)

## Slide 7: Given transmission limited capacity, national energy markets cannot be perfectly coupled 8760h every year
Why to split EU D-A energy market?
  EU market is split when transmission capacity is constrained (i.e., when there is a congestion)
Cross-border congestion management calls for coordination (coupling/decoupling) of D-A energy markets

## Slide 8: 2 options to coupling/decoupling D-A EU el. energy markets?
Explicit auctions
  Cross-border transmission capacity is a separate market
  Cross-border integration of energy markets is left to the ability of arbitrageurs
Implicit auctions (market coupling or market splitting)
  Algorithm common to Power Exchanges & TSOs allocates cross-border capacity according to energy bids’ merit order
Day-ahead
Market
(energy B)
Day-ahead
Market
(energy A)
Day-ahead
Market
(transmission A-B)
Day-ahead
Markets
of both countries
(energy A + B)
Matching
Algorithm
Allocates
transmission
capacity A to B
to best A+B
energy bids
Explicit auctions
Implicit auctions
Country B
Country A

## Slide 9: A landmark: EU Day-ahead market coupling
Coupled DA-markets in the EU (ENTSO-E, 2017)
MRC= Multi regional coupling
MC= Market coupling

## Slide 10: How integrated are EU Day-Ahead energy markets within Market Coupling?

## Slide 11: The complete set of EU wholesale el. markets
Sequence of wholesale el. markets
Short-term Energy markets
Short term
Reserves/
flexibility markets
Delivery by injection
Time
T-~24h
T
Short term Transmission markets
Energy
Transmission
Flexibility Reserves
Real time /
Balancing
Mechanism
(centralised
by the TSO)
Long-term Energy markets
Long-term
Reserves/
flexibility markets
T-~months/years
Long-term Transmission markets
T-~2h
Electricity component
NB: markets for flexibility are often called “reserves” because the TSO reserves some flexible capacity (power station or demand response) to ensure enough flexibility in real time
Energy
Transmission
Reserves / flexibility
Scope

## Slide 12: [2] Network Codes as EU Market Design

## Slide 13: What is a EU network (code or guideline)?
1
2
3
4
A set of practical rules applied to cross-border & market integration issue
Developed by gathering of NRAs into ACER, of TSOs into ENTSO-E + Control by the European Commission (under Art. 8 of Electricity Directive 2009)
Going through a EU law-making process called ‘Comitology’
Adoption transforms network codes & guidelines proposals into binding “EU laws” as “Regulations” to be implemented in all EU countries by all NRAs & TSOs

## Slide 14: Which EU electricity network codes?
How to integrate power markets?
Market codes
Forward Capacity Allocation (FCA GL)
Capacity Allocation and Congestion Management (CACM GL)
How to harmonize grid connection rules?
Grid connection codes
Demand Connection Code (DCC NC)
Requirements for Generators (RfG NC)
How to seamlessly operate a power system?
System operation codes
System Operations (SO GL)
Emergency and Restoration (ER NC)
Electricity Balancing (EB GL)
HVDC Connections (HVDC NC)

## Slide 15: Operations codes: e.g. towards regional operation?
Regional Security Centres (ENTSO-E, 2017)
Synchronous zones in the EU (ENTSO-E, 2017)

## Slide 16
Notes: LEO

## Slide 17: Network codes course at Florence School (Content)

## Slide 18: [3] Mid term EU generation adequacy forecast 2017

## Slide 19: 2020 Loss of load expectations (LOLE) – base case
Loss Of Load Expectation (h/y) LOLE is the number of hours in a given period (year) in which the available generation plus import cannot cover the load in an area
Main risk of resource scarcity:
• Islands
(e.g. Cyprus, Malta, Ireland and Northern Ireland)
• periphery*
(e.g. Albania, Bulgaria, Greece and Finland)
* Periphery to simulated countries of continental Europe

## Slide 20: 2025 Loss of load expectations (LOLE) – base case
Island/ periphery risk confirmed
Belgium and Baltics risk appear

## Slide 21: Mothballing sensitivity leads to large uncertainty and thereby strong interdependency
Mothballing in 45% of the countries significantly impacts adequacy in 82% of the countries
Importance to have reliable generation plan from utility (min 3-5 years)
Crucial to get a clear picture
Significant impact on adequacy in a larger region
Coordinated studies needed
Notes: Substantial capacities at risk of being mothballed, with far-reaching consequences for adequacy: In our data collection, 45% of the countries reported generation capacities at risk of being mothballed, representing a reduction of thermal generation capacity by 15% compared to the base case (best estimate). In a sensitivity simulation analysing adequacy in Europe without these capacities, significant impacts are observed. In fact, these mothballing activities would imply tightened adequacy margins in 82% of the countries, thus having a substantial effect far beyond national borders. It will therefore be crucial to monitor mothballing activities on a broader European scale.

## Slide 22: Proposal new EU energy law (“Package”)
Clean Energy Package:
“Where the European resource adequacy assessment identifies a resource adequacy concern; Member States shall identify any regulatory distortions that caused or contributed to the emergence of the concern”
Strong Pan-European and technological interdependencies.
Need to coordinate and align activities

## Slide 23: [4] Ten Year Network Development Plan

## Slide 24: Ten Year Network Development Plan (TYNDP)
Long-term network development plan is one of the core missions of any transmission system operator (TSO).
It allows them to tailor grids to the evolution of demand and generation, securing an affordable supply of energy for customers in the next decades.
Having a European approach to grid planning ensures consistency and cost-efficiency.
The TYNDP is thus key to many of Europe’s economic, climate and energy objectives.

## Slide 25: Ten year network development plan
ENTSOs for electricity & gas pooled their efforts and expertise to provide a joint set of scenarios, allowing for assessments of future investment decisions in Europe to be based on comparable analysis between the sectors. Together, we described three markedly different and ambitious paths towards delivering the future European emission targets
Scenarios
Short term and medium term
  2020
  2025 Coal Before Gas (CBG) and 2025 Gas Before Coal (GBC).
Long terms :
  Sustainable Transition (ST) Targets reached through national regulation, emission trading schemes and subsidies, maximising the use of existing infrastructure.
  Distributed Generation (DG) Prosumers at the centre – small-scale generation, batteries and fuel switching society engaged and empowered.
  Global Climate Action (GCA) Full speed global decarbonisation, large-scale renewables development in both electricity and gas sectors.
  External Scenario: Based On EUCO 30 EUCO 30 is a core policy scenario produced by the European Commission. The scenario models the achievement of the 2030 climate and energy targets as agreed by the European Council in 2014, but including an energy efficiency target of 30%. The ENTSOs both welcome this new collaboration with the European Commission and welcome further cooperation.

## Slide 26: Ten year network development plan

## Slide 27: Ten year network development plan

## Slide 28: TYNDP 2018– Scenario results- electricity demand

## Slide 29: TYNDP 2018– Scenario results- electricity demand

## Slide 30: TYNDP 2018– Scenario results- electricity supply

## Slide 31: TYNDP 2018– Scenario results- electricity supply

## Slide 32: TYNDP 2018– Scenario results- Increase in RES

## Slide 33: TYNDP 2018– Scenario results- emission reductions

## Slide 34: TYNDP 2018– Scenario results- marginal cost

## Slide 35: TYNDP 2018– Projects – Mid term

## Slide 36: TYNDP 2018– Projects – Long term

## Slide 37: TYNDP 2018– Projects – Future

## Slide 38: TYNDP 2018– Projects – All projects

## Slide 39: [5] Other Changes are coming: Tomorrow 

## Slide 40: Many thanks for your patience!

## Slide 41
Dhanyavad!
Email : jean-michel.glachant@eui.eu
Tweeting no Twitter: @JMGlachant >44 000 tweets
Web site: http://fsr.eui.eu/